## Slide 1
Deep learning for System Identification
Introduction
Marco Forgione, Dalle Molle Institute for Artificial Intelligence, USI-SUPSI, Lugano, Switzerland Milano, June 30, 2025
Slides originally prepared by: Dario Piga, Dalle Molle Institute for Artificial Intelligence, Lugano, Switzerland

## Slide 2
Introduction to System Identification

## Slide 3
Models
Abstractions of reality
Models can describe mechanical systems, social interactions, markets, etc.
Different types of models:
  Intuitive/mental models
  Graphical models (Bode diagrams, flowcharts)
  Mathematical models describing relations between variables/signals of the system/process

## Slide 4
Modelling paradigms
First principles modelling (from first principles laws of physics/chemistry/biology, etc.)
  Pure physical modelling: white-box approach
  Knowledge of the physics behind the system/process
  Models are interpretable
  Sometimes, physical modelling can be complex or even impossible
Data-driven modelling (from measurements of variables gathered from experiments)
  Pure data-driven modelling: black-box approach
  Limited knowledge of the system/process
  Models are usually not explainable
  Need for (informative) data
  Generalization properties might be limited
Combination of first principles and data-driven modelling is also possible
  E.g., model structure derived from physics, and some parameters estimated from data
  In any case, even pure physical models needs often to be validated with experiments

## Slide 5
Dynamical systems
Systems with memory (present also depends on the past)
S
y
u
Described by equations evolving in time
Continuous time: ODE
Discrete time: Recurrence equation

## Slide 6
Model structures
Model: Given past inputs and outputs, provides an estimate of the current output
  Example: AutoRegressive eXogenous (ARX) model
Residual signal:
  Example:
Loss:
  Example: least-squares loss:

## Slide 7
Least squares estimate: ARX model structure

## Slide 8
Example: Cascaded Tanks System
Schoukens, M. et al. "Cascaded tanks benchmark combining soft and hard nonlinearities." Workshop on nonlinear system identification benchmarks, 2016.
https://www.nonlinearbenchmark.org/
Fluid level control system with two tanks
Upper tank fed by a pump
Water flows from upper tank to lower tank through a small opening
Water flows from lower tank to reservoir through a small opening
Overflow in the upper tank may happen
Input: pump voltage
Output: water level of lower tank
Length of training set: 1024 samples
Length of test set: 1024 samples
Sampling time: 4 s
Metrics (over test data) both for 1-step and open-loop simulation:
Jupyter Notebook: cascaded_tanks (Part 1)

## Slide 9
Including nonlinearities
  Linear-in-the-parameter NARX model:
  is a vector function of containing (known) nonlinear elements, e.g.,
How to choose the non-linearities?
  General NARX model:
- is a nonlinear function (e.g., neural network) of past observations
- Linearity in θ is lost

## Slide 10
Limitations of (N)ARX models
Prediction error only looks one-step ahead
In case of data sampled at high-frequency, a good one-step ahead predictor could be:
We would like to have predictive models that provide good prediction in a long-horizon

## Slide 11
Simulation error minimization
Linear models
  Output Error (OE) model:
Residual signal:
Loss: sum of squared residuals is no longer convex!

## Slide 12
First-order methods for non-convex optimization
Other updates are possible, e.g., gradient-descent with momentum:
Vanilla Gradient Descent
Jupyter Notebook: cascaded_tanks.ipynb (Part II)

## Slide 13
Convergence of gradient-descent
Assumptions:
Convergence:
Karimi, H., Nutini, J., & Schmidt, M. (2016, September). Linear convergence of gradient and proximal-gradient methods under the Polyak-Lojasiewicz condition. In Joint European conference on machine learning and knowledge discovery in databases (pp. 795-811). Cham: Springer International Publishing.

## Slide 14
Stochastic Gradient Descent
Uniformly randomly sampled from {1,2,…N}
Mini-batch gradient descent (B<<N):
Do not process the whole dataset to update the model parameters, just process a smaller batch of samples and then make the update
1 iteration = 1 parameter update
1 epoch = parameter updates
Bottou, L., Curtis, F. E., & Nocedal, J. (2018). Optimization methods for large-scale machine learning. SIAM review, 60(2), 223-311.

## Slide 15
Enforcing sparsity: L1-regularization
Linear-in-the-parameter NARX model:
L1 regularization (LASSO-like): penalize model complexity during training

## Slide 16
Non smooth functions
Parikh, N., & Boyd, S. (2014). Proximal algorithms. Foundations and Trends® in Optimization, 1(3), 127-239.

## Slide 17
Proximal gradient methods
non-differentiable convex funtion
Proximal operator of function R() with parameter
Fixed point equation

## Slide 18
Fixed point equation: proof of stationarity
We only prove in one direction:
By definition of the proximal operator:
The minimized function is convex: smooth quadratic + non-smooth yet convex term. Its optimality condition is:

## Slide 19
Proximal gradient methods: constrained optimization
Example: R(θ) indicator function of a convex set :
orthogonal projection
This leads to the projected gradient descent algorithm:

## Slide 20
Proximal gradient methods: L1 regularization

## Slide 21
Proximal gradient methods: algorithm L1-regularization
Jupyter Notebook: cascaded_tanks.ipynb (Part III)