## Slide 1
Neural State-Space models
Exercises
Marco Forgione, Dalle Molle Institute for Artificial Intelligence, Lugano, Switzerland
Lugano, April, 23rd, 2024

## Slide 2
Physics-inspired neural state-space models
Cascaded tanks system. Input: upper tank inlet flow u. Output: lower tank level.
The dataset has just T=1024 time points. We implement full simulation error minimization.
Schoukens, M. et al. "Cascaded tanks benchmark combining soft and hard nonlinearities." Workshop on nonlinear system identification benchmarks, 2016.

## Slide 3
Physics-inspired neural state-space models – model #1
Cascaded tanks system. Input: upper tank inlet flow u. Output: lower tank level.
Intuitive physics:
The system has two states: levels
The state is measured:
State does not depend on
State does not depend on directly

## Slide 4
Physics-inspired neural state-space models – model #2
Cascaded tanks system. Input: upper tank inlet flow u. Output: lower tank level.
Intuitive physics:
The system has two states: levels
The state is measured:
State does not depend on
State does not depend on directly

## Slide 5
Physics-inspired neural state-space models – model #3
Cascaded tanks system. Input: upper tank inlet flow u. Output: lower tank level.
Intuitive physics:
The system has two states: levels
The state is measured:
State does not depend on
State does not depend on directly (according to the benchmark description, water overflows from the upper to the lower tank. Thus, there is a direct term from u to )

## Slide 6
Simulation error minimization – model #1
Let us implement simulation error minimization
Where and are generic feed-forward neural networks with:
(not a choice, dimensionality constraint)
(as known from the physics)
One hidden layer
Tanh non-linearity
64 hidden units
NOTE:
You should train with respect to both and .
In test, exploit the additional knowledge from the benchmark info that is the same in the two experiments.

## Slide 7
PyTorch Implementation (hints)
Code adapted from https://github.com/forgi86/pytorch-ident
Custom state-update function
Custom code to unroll over time
Notes: https://github.com/pytorch/examples/blob/main/word_language_model/main.py

## Slide 8
PyTorch Implementation (hints)
Initializations
Define model and initial state
Define optimizer
Compute loss (in a trainig loop…)
Notes: https://github.com/pytorch/examples/blob/main/word_language_model/main.py

## Slide 9
Simulation error minimization – model #2
Let us implement simulation error minimization
Where is a generic feed-forward neural networks and the second state is observed:

## Slide 10
Simulation error minimization – model #3
Let us implement simulation error minimization
Implement and train a tailor-made architecture consistent with all the physics constraints assumed for model #3:

## Slide 11
Thank you for your attention